## Slide 1: Nano-Material Identification using Fluorescence Lifetime Imaging Microscopy
Ryan Beams
DIDSR, FDA, Silver Spring, MD
Oct 10, 2018
Delay
(phase)
z2
z1
z2
QEEN II Oct 9-10, 2018

## Slide 2
Motivation for Fluorescence Lifetime Imaging
Fluorescence Lifetime
High Resolution Imaging
10um
+
Advantages of Fluorescence Lifetime Imaging Microscopy (FLIM):
Excited state dynamics information
Generally non-destructive and non-contact
Sub-micron lateral resolution
Works in ambient conditions
Robust: Not dependent on concentration, excitation power, or photo-bleaching
Sensitive to the local chemical and environmental changes: pH, degrees of freedom, refractive index.
Notes: 300 nm beads conv. On left and SR on the right. Lots of neat stuff here..seperate beads, couning beads in islands etc..

## Slide 3: Local Environment and Quantum Yield
Fermi’s Golden Rule
Purcell Effect
quantum yield
radiative rate
lifetime
non-radiative rate
Local environment influences the quantum yield of an emitter
Emission
Photon
Excitation
Photon
Non-radiative Decay
Fluorescence
Decay Rate
Metal Surface
Emitter
Drexhage, J. of Lumin. (1970)
Separation Distance

## Slide 4
Linear vs Two-Photon Fluorescence
Two-Photon Fluorescence Lifetime
Courtesy of Tana Villafaña
Linear Fluorescence Lifetime
Advantages of Two-Photon Fluorescence
- Less scattering (i.e. deeper penetration)
- Only excite fluorescence in focus (free confocality)
- Less photo-damage
http://candle.am/microscopy
Notes: 300 nm beads conv. On left and SR on the right. Lots of neat stuff here..seperate beads, couning beads in islands etc..

## Slide 5
Two Photon Fluorescence Lifetime Imaging
Notes: 300 nm beads conv. On left and SR on the right. Lots of neat stuff here..seperate beads, couning beads in islands etc..

## Slide 6: Applications of Fluorescence Lifetime
Orte, et al. ACS Nano (2013)
Lifetime Detection of pH
Schell, et al. Nano Letters (2014)
Local Density of States Imaging
Chemical Bonds
Intrinsic Lifetime
Semiconductor
Pigments
Woodcock, Beams, et al. Adv. Mat. Inter. (2017)

## Slide 7
Identifying Nano-Materials
White Pigments and Fillers
CaCO3
TiO2
ZnO
BaSO4
Ag Nano-Particles
X Ray
FLIM
Metal Oxide Particles

## Slide 8
Acknowledgements
Stephan Stranick (NIST)
Ed Vicenzi (SI)
Keana Scott (NIST)
Jeff Gilman (NIST)
Jeremiah Woodcock (NIST)
Chelsea Davis (NIST)
Thank you!
Ryan.Beams@fda.hhs.gov